## Slide 1: OEM specific HID architecture overview
HU
HS
SDL app
Unnecessary to customize for each HU’s special device
Easy to migrate iOS/Android app to SDL VPM support
Unnecessary to draw focus highlight
Unnecessary to control focus movement (If app hope to control then, it may be controlled)
If Apps using themselves UI/Widget (current Sygic app) then Apps must be customized with using each plugin directly.
SDL core
Unnecessary to add new RPC (SDL Core 4.4 can be used)
SDL HMI
Handle HU specialized device. Properly interpret special devices’ event to SDL RPC. If required, proprietary RPC shall be used. The RPC can be handled by proper plugin.
Specific Device
High-level UI/Widget library
This module will be extended / modified from iPhone: XXXX, Android: Virtual Display Encoder.
Provide functionality of retrieving View/Widget hierarchy for RHID plugin.
Remote Human Interface Device manager
provide pluggable architecture
select proper plugin for connected HU type, in runtime
------ Remote Human Interface Device plugin I/F -----
Lexus Remote Touch plugin
This layer’s roles and abilities are:
Share layout information to HU, if required. Layout information will be created with using “High-level UI/Widget library”
Overlay focus highlight to rendered image, before encoding, if required. Each plugin will draw in HS layer (or not draw in HS, but draw in HU) to be followed to each OEM’s spec.
Exchange information from HU/HS to HS/HU with using new RPC for exchange some of proprietary information to HU (SendOEMSpecificData)
Convert HU OnTouch or other RPC to proper OnTouch, if required.
Each OEM/Tier1s should provide plugin to support their special device.
Encoder
Notify High-level UI event as not SDL event but iPhone/Android OS event
Provide High-level UI/Widget
Mazda Commander Control plugin
Bypass
Others
SDL proxy

## Slide 2: OEM specific HID architecture Alternative#1
Alternative #1: No new RPCs are added to support the plug-in interface. Rather, SystemRequest and other existing RPCs will be repurposed. Since the custom behaviors will be encapsulated in the plug-in and will only work in the repurposed way with the OEM head unit, there is no impact on other SDL implementations.
HU
HS
SDL app
Unnecessary to customize for each HU’s special device
Easy to migrate iOS/Android app to SDL VPM support
Unnecessary to draw focus highlight
Unnecessary to control focus movement (If app hope to control then, it may be controlled)
If Apps using themselves UI/Widget (current Sygic app) then Apps must be customized with using each plugin directly.
SDL proxy
SDL core
Unnecessary to add new RPC (SDL Core 4.4 can be used)
SDL HMI
Handle HU specialized device. Properly interpret special devices’ event to SDL RPC. If required, proprietary RPC shall be used. The RPC can be handled by proper plugin.
Specific Device
High-level UI/Widget library
This module will be extended / modified from iPhone: XXXX, Android: Virtual Display Encoder.
Provide functionality of retrieving View/Widget hierarchy for RHID plugin.
Remote Human Interface Device manager
provide pluggable architecture
select proper plugin for connected HU type, in runtime
------ Remote Human Interface Device plugin I/F -----
Lexus Remote Touch plugin
Mazda Commander Control plugin
Bypass
This layer’s roles and abilities are:
Share layout information to HU, if required. Layout information will be created with using “High-level UI/Widget library”
Overlay focus highlight to rendered image, before encoding, if required. Each plugin will draw in HS layer (or not draw in HS, but draw in HU) to be followed to each OEM’s spec.
Exchange information from HU/HS to HS/HU with using existing RPC, SystemRequest and other existing RPCs.
Convert HU OnTouch or other RPC to proper OnTouch, if required.
Each OEM/Tier1s should provide plugin to support their special device.
Encoder
Notify High-level UI event as not SDL event but iPhone/Android OS event
Others
Provide High-level UI/Widget

## Slide 3: OEM specific HID architecture Alternative#2
HU
HS
SDL app
Unnecessary to customize for each HU’s special device
Easy to migrate iOS/Android app to SDL VPM support
Unnecessary to draw focus highlight
Unnecessary to control focus movement (If app hope to control then, it may be controlled)
If Apps using themselves UI/Widget (current Sygic app) then Apps must be customized with using each plugin directly.
SDL proxy
SDL core
Unnecessary to add new RPC (SDL Core 4.4 can be used)
SDL HMI
Handle HU specialized device. Properly interpret special devices’ event to SDL RPC. If required, proprietary RPC shall be used. The RPC can be handled by proper plugin.
Specific Device
High-level UI/Widget library
This module will be extended / modified from iPhone: XXXX, Android: Virtual Display Encoder.
Provide functionality of retrieving View/Widget hierarchy for RHID plugin.
------ Remote Human Interface Device plugin I/F ----- as RPC
OEM specific device controller
This layer’s roles and abilities are:
Create layout information with using RHID I/F(as RPC), if required. Layout information will be created with using “High-level UI/Widget library” as RPC
Overlay focus highlight to rendered image, after decoding, HS app should not draw focus highlight, anything.
Each OEM/Tier1s must implement in SDL HMI to support specific device to use RPC.
Encoder
Notify High-level UI event as not SDL event but iPhone/Android OS event
Provide High-level UI/Widget
Alternative #2: All of I/F which plug-in requires, will be implemented as MOBILE RPC. Plugin architecture will not be required, SDL HMI may be implemented OEM specific device control with using these RPC. However, this functionalities may be depend on Android/iOS architecture. So, it will be difficult to generalize because of another architecture.